## Slide 1: ASIC Implementation of Horn & Schunck Optical Flow Algorithm
Pi-Feng Chiu
Ying Qiao

## Slide 2: Motivation
Optic flow gives important information for building large computer vision system
CMOS IC technology keeps further scaling
  ASIC implementation of optic flow algorithms benefits from all these process advancements
Tradeoffs between power and area at certain frame rate
We will focus on
  Horn & Schunck algorithm
  Low power design

## Slide 3: Optical Flow Algorithm
Calculate the spatial and temporal differences between frames
  Horn & Schunck, gradient-based algorithm
[Ref] Jose L. Martin, Aitzol Zuloaga, Carlos Cuadrado, Jesus Lazaro, Unai Bidarte, “Hardware implementation of optical flow constraint equation using FPGAs,” Computer Vision and Image Understanding, 2005, pp. 426-490.

## Slide 4: Architecture
Block diagram and main computing flow
N = 8

## Slide 5: Design Considerations
Target performance specifications:
  Frame size: 720*480 pixels
  Frame rate: 60 frame/s
  Throughput: 20250 Kpixel/s
Our main design objective is to lower the energy consumption by investigating several architectural approaches.
  Parallel computing blocks for pixel block operations
  Iteration number choice optimization
  Multi-VT design scheme to reduce leakage power consumption.
  RAM blocks allocation will be further explored

## Slide 6: Timetable
10/04/12 | Initial Project Proposal Presentation
10/11/12 | Define all the signals and define all the functional blocks
10/18/12 | Design sub-blocks and the testbenches
10/25/12 | (Presentation)
11/01/12 | Finish all functional blocks
11/08/12 | (Presentation)
11/15/12 | Connecting all modules and test with contract
11/22/12 | Power/area/delay analysis
11/29/12 | Design Wrap up
12/07/12 | Final Project Presentation
12/12/12 | Final Project Report